## Slide 1: Framework Data Development and Web Map Services
WV GIS Technical Center
27 Nov 2012 Kurt Donaldson

## Slide 2: Framework Data Report
Framework Data
WVGISTC Website http://www.wvgis.wvu.edu/resources/resources.php?page=dataProductDevelopment/baseLayers

## Slide 3: Internet Map Services – Public Demand
Question: Does WV offer interactive mapping that includes layers such as: Parcels, Roads, ROW, Subdivisions, Land marks, etc that the public can search? I'm particularly interested in Wayne County. Ohio offers the following resource – http://www.dalisproject.org/pages/imsweb.htm. The general tab will take you to the interactive map.
Thanks,
Jerrit Delaware County, Ohio 26 November 2012

## Slide 4: Statewide Imagery
Statewide Digital Imagery
1996-99 USGS DOQQ, 1-meter CIR, leaf off
2003 SAMB, 2-ft natural color, leaf off
2007 USDA NAIP, 1-meter, leaf on, natural color & CIR
2009 USDA NAIP, 1-meter, leaf on, natural color
2011 USDA NAIP, 1-meter, leaf on, natural color & CIR
2010-12 WV Sheriff Association (Pictometry), 1-ft (4” urban areas) natural color, mostly leaf-off, oblique and orthogonal imagery, license restrictions
Web Map Services (Viewing Only)
WV DNR: http://tagis.dep.wv.gov/mapservices2.html
WVGISTC: http://services.wvgis.wvu.edu/ArcGIS/rest/services

## Slide 5: WV Sheriffs Association Imagery
WVGISTC Web Map Service
Web: http://services.wvgis.wvu.edu/ArcGIS/rest/services
ArcMap: services.wvgis.wvu.edu/ArcGIS/services

## Slide 6: 2010-11 WV Sheriffs Imagery (12 “)
Statewide Web Service

## Slide 7: WV Sheriffs Imagery – 12” & 4”
Scale 1:1,128
12 inch
4 inch

## Slide 8: WV Sheriffs Imagery – 12” & 4”
Scale 1:282
12 inch
4 inch

## Slide 9: WV Sheriffs Imagery – 4”
Find the horse?
4 inch

## Slide 12: Statewide Imagery (Cont.)
Statewide Leaf-Off Imagery Mosaic (Best-Available Leaf Off) ** Imagery compiled from county and others sources **
Bluestone Lake (USACE, 2009)
Cabell County (2009)
Brooke County (2007)
Hancock County (2007)
Monongalia County (2010)
Raleigh County (2011) Some counties make their 6” imagery available in the public domain, other counties for viewing as a Web map service only.
WVGISTC Web Map Service
Web: http://services.wvgis.wvu.edu/ArcGIS/rest/services
ArcMap: services.wvgis.wvu.edu/ArcGIS/services

## Slide 13: Best Leaf-Off Imagery
High resolution imagery for Charleston, Huntington, Morgantown, and Weirton areas incorporated into SAMB 2003 statewide leaf-off imagery
Recently Received a Broadband Grant to Update Best Leaf-Off Imagery Service

## Slide 14: Best Leaf-Off Imagery – Monongalia County
2010 High Resolution Imagery (1” = 100’, 0.5 ft. pixels) Marilla Park, Morgantown, WV
See the people?

## Slide 16: Parcel Web Map Service
WVGISTC Web Map Service
Web: http://services.wvgis.wvu.edu/ArcGIS/rest/services
ArcMap: services.wvgis.wvu.edu/ArcGIS/services

## Slide 17: Parcel Query

## Slide 18: Parcels Availability for Web Map Service
Surface tax parcels provided by counties
For viewing purposes only

## Slide 19: Streams Maintenance
(1) 1:24K National Hydrography Dataset (NHD). USGS funded maintenance for 74 miles across 143 NHD features within the Gauley River watershed. New NHD editing tools utilized. (2) 1:4800 SAMB Local Resolution (2003)

## Slide 20: NHD Steams Updated in Mined Areas
Mined area with effected streams marked (red)
2,000 High Resolution NHD features with an estimated length of 800 miles have been impacted by surface mining and require editing.

## Slide 21: Steams Updated in Mined Areas
Mined area with effected streams marked (red)
USGS funded project

## Slide 22: Geographic Names Updated
arenas
auditoriums
bridges
cemeteries
city and town halls
convention and conference centers
courthouses
fire stations
golf courses
hospitals
libraries
museums
police stations
post offices
prisons
schools
shopping centers
stadiums
summits
theaters
USGS funding updated 20 GNIS cultural feature classes, including 3,773 features identities

## Slide 23: Zoom to Geographic Name

## Slide 24: WVDOT Trails Database (iPad)

## Slide 25: Address Labels as Reference Layer

## Slide 26: West Virginia Site & Street Locator Services
Build Reference Data
Extract data from SAMS
Create statewide point and street reference files
Build Locator Services
Publish WV Site (point) and WV Street Locator Services
Search
Addresses
Customized Applications (WV Flood Tool)
Search by Table
Update and enhance address locators
Search by individual address
Geocoding Services created from WVDHSEM Statewide Addressing & Mapping System

## Slide 27: Zoom to Address

## Slide 28: Search on Address
Address Match with WV Site Locator
Search on Address

## Slide 29: Other Framework Data Notes
Statewide Roads
  Major Roads from WV DOT
  Local Roads from Census 2010
Boundaries (county, municipal)
  WVAGP sponsored BAS training in 2012
Land Cover
  WV DNR/NRAC created new land cover from 2011 NAIP
Elevation
  WVDEP/WVU NRAC have collected LiDAR for 96% of southern coalfields.
    Coverage and Metadata: http://tagis.dep.wv.gov/lidar.
    Download from WV View: http://www.wvview.org
  WV DEP created aggregate hillshade Web map service
  WVGISTC created 10 ft. contour Web map service
Framework data layers are often published as
Web map services

## Slide 30: Consuming Web Map Services
Online Application
Commercial Map Services (ESRI, Bing)
Geocoding Services (state and national sources)
Geoprocessing & Query Map
Services
WV Map & Web Services
(WV DHSEM, WV DEP, WVGISTC)
GIS Data from federal, state, and local agencies

## Slide 31: MapWV Viewer (Shared Services)
Shared Data Services Seamless to Users
CIR image and roads consumed from WV DEP & WV DOT Servers

## Slide 32: Questions???
Kurt Donaldson
WV GIS Technical Center
kdonalds@wvu.edu
(304) 293-9467